## Slide 1
8237 DMAC
Direct Memory Access Control

## Slide 2
Why ???
There is no direct connection between memory and I/O.
Processor
Memory
I/O
DMAC
8237
Whenever data transfer take place need to generate control signals ( RD bar and WR bar) In between memory and IO devices no one is responsible to generate control signals.
Processor is by default bus master and responsible to generate control s/g like IO read/write , memory read/write.
As a programmer we want to transfer a byte from memory to I/O device, that byte first travel to the processor and then it will transfer to IO device.
Hence to transfer data between memory and IO device processor required two m/c cycles:
1. read data from memory i.e. MEMRD
2. write data into IO device using IO write m/c.
If minimum no. of data transfer is there then 8086 can transfer, but if there is bulk of data like print a file or copy of file then 8086 is not a feasible solution.
We need a device which is responsible to direct transfer the data between memory and IO devices. And that device is also responsible to generate control signals.
Assume that there is no DMAC, processor has to perform this data transfer between memory and I/O devices.
For above data transfer , first instruction is to read data from memory and second to write into I/O
ex. Mov al/ax, [si]
OUT I/O
inc SI
dec counter
repeat above 4 steps till counter will become zero.
If we want to transfer 1000 bytes then we have to repeat these 5 instructions 1000 times.
For execution of 1 instruction : Fetch – Decode - Execute
For execution of 5 instructions 1000 times : 5000 time Fetch – 5000 Decode - 5000 Execute
Hence 8237 DMAC is used which is hardwired to do transfer.

## Slide 3
1. By default a processor is a bus master. If 8237 DMAC wants to become bus master it has to send HOLD = 1 to 8086.
Processor
Memory
I/O
DMAC
8237
HOLD = 1
HLDA = 1
2. After receiving HOLD =1 , processor enters into hold state ( release the control of bus)
4. Now DMAC become bus master it will allow transfer between memory and I/O devices.
Latch
3. Processor send HLDA = 1 to 8237.
5. After finishes the data transfer 8237 DMAC send HOLD = 0 to 8086
HOLD = 0
6. 8086 gain become the bus master.
8237 DMAC Process

## Slide 4
Example : Print “n” no. of bytes.
Who wants to perform data transfer (print) ?
DMAC
8086
Who knows about data transfer (print) ?
DMAC
8086
As a programmer we are going to instruct processor to print.
8086 will inform to DMAC about the data transfer.
There are internal 2 registers of DMAC :
1. CAR – Current Address Register
2. CWCR – Current Word Count Register
It is used to store the starting address of data.
It is used to store the no. of bytes.

## Slide 5
Real time Example :
As a programmer we are going to right click on file and select print option.
Processor is going to inform DMAC about this printing and will provide the starting address and no. of bytes.
CAR = 4000 and CWCR = 0005
What if there is no printer????
After receiving starting address and data count DMAC not directly send
HOLD = 1 to 8086.
It will wait for confirmation from I/O devices called DREQ ( data request). If DREQ = 1 which means device is ready for transfer. Hence DREQ is always 1.
Which means I/O devices are always ready for transfer.
Now DMAC send HOLD =1 , after receiving HLDA from 8086 DMAC will become bus master, but before transferring the data it will give acknowledgment to I/O device through DACK bar (to wake up the I/O device)
Within 5 clock cycles data transfer is done between DMAC and I/O device. Address is auto increment.
When Transfer is over DMAC send HOLD =0.
Processor
Memory
I/O
DMAC
8237
DREQ = 1
HLDA
Latch
HOLD
DACK

## Slide 6: Types/Methods :
Block Transfer
Cycle Stealing
Demand Transfer
Hidden Mode