## Slide 1
Block 1
Block 2
Block Exchange
Block 1
Block 3
1
Block 2
3
2
Without String Instruction
With String Instruction
Without String Instruction
With String Instruction

## Slide 2
Block Exchange without string instruction
WAP to exchange 05 data bytes present at two memory blocks 1000 and 2000 onwards respectively without using string instructions
1000 | 01
1001 | 02
1003 | 03
1004 | 04
1005 | 05
Block 1
Block 2
2000 | 05
2001 | 04
2003 | 03
2004 | 02
2005 | 01
SI
DI
[SI] = 01 & [DI] = 05
Mov content of SI in AL & content of DI in AH
AL = 01 & AH = 05
Exchange the content of AL and AH
AL = 05 & AH = 01
Store the exchanged value into the blocks
Increment SI and and DI by 1 to point next memory location
SI+1
DI+1

## Slide 3
DI
DS
SI
Block Exchange string instruction
WAP to exchange 150 data bytes present at two memory blocks 45000 and 38000 onwards respectively using string instructions
3000
45000
38000
63000
4000
5000
6000
3000
8000
1
2
3
DS
SI
ES
DI
DS
SI
ES
DI
ES

## Slide 4
Code for 1st transfer : | Code for 2nd transfer : | Code for 3rd transfer :
Mov ax, 4000 | Mov ax, 3000 | Mov ax, 6000
Mov ds, ax | Mov ds, ax | Mov ds, ax
Mov ax, 6000 | Mov ax, 4000 | Mov ax, 3000
Mov es, ax | Mov es, ax | Mov es, ax
Mov si, 5000 | Mov si, 8000 | Mov si, 3000
Mov di, 3000 | Mov di, 5000 | Mov di, 8000
Mov cx, 150 | Mov cx, 150 | Mov cx, 150
Cld | cld | Cld
REP Movsb | REP Movsb | REP Movsb
3000
45000
38000
63000
4000
5000
6000
3000
8000
1
2
3
DS
SI
ES
DI
DS
SI
ES
DI
DS
SI
ES
DI