## Slide 1: Create an array using TASM

## Slide 2
Array
Element 1
Element 2
Element 3
Element 4
Address of an
Element 1
Address of an
Element 2
Address of an
Element 3
Address of an
Element 4
04
01
07
03
Array is stored into the data segment, hence each element having address.
SI is the pointer for data segment.
SI
SI + 1
SI + 2
SI + 3
SI | 2001 | 04
SI+1 | 2002 | 01
SI+2 | 2003 | 07
SI+3 | 2004 | 03
DS
Assign offset address of an array to SI pointer.
SI
=
2001
[SI]
=
[2001]
=
04
[SI] = 04
[SI+1] = 01
[SI+2] = 07
[SI+3] = 03
Steps to create an array :
Create an array variable and put elements into it :
Arr db 04,01,07,03H
Assign offset address with SI pointer:
Mov si , offset Arr
OR
LEA si , Arr
Transfer first element of an array into reg :
Mov al , [ si ]
For next element :
Mov al , [ si + 1 ]
OR
Inc si
Mov al , [ si ]

## Slide 3: WAP to create an array and print all elements of an array
.model small
.data
arr db 05,05,03,04,05h
.code
mov ax,@data
mov ds,ax
mov si , offset arr or lea si, arr
mov dh,05h
back: mov al,[si]
inc si
mov ch,02h
mov cl,04h
mov bh,al
i2: rol bh,cl
mov dl,bh
and dl,0fh
cmp dl,09
jbe i4
add dl,07h
i4: add dl,30h
mov ah,02h
int 21h
dec ch
jnz i2
mov dl,' '
mov ah,02h
int 21h
Initialization of an array
Counter for an elements
Mov first element into al
Increment SI pointer by 1 to point next element
Assign offset address
Print first element using 30-37 logic
Assign blank space between two element
dec dh
jnz back
mov ah,4ch
int 21h
end
Decrement counter of an element, if zero then terminate program else print second element
1
DS
SI | 2001 | 05
SI+1 | 2002 | 05
SI+2 | 2003 | 03
SI+3 | 2004 | 04
SI+4 | 2005 | 05
2
3
Dh = 05
4
Al =
05
5
0
5
5
6
Dh = 04
0
5
Al =
05
Dh = 03
Al =
03
0
3
Dh = 02
Al =
04
0
4
Dh = 01
Al =
05
0
5
Dh = 00
Terminate program