## Slide 1: Instruction set of 8086

## Slide 2
Instruction set of 8086
1
2
3
4
5
6

## Slide 3: 1. Data transfer group
MOV
PUSH
POP
XCHG
XLAT
IN
OUT
LEA
LDS
LES
LAHF
SAHF
PUSHF
POPF
1.1
1.2
1.3
1.4
1

## Slide 4: 1.1 General Purpose
General purpose
MOV
PUSH
POP
XCHG
XLAT

## Slide 5: MOV Instruction
The mov instruction copies a word or a byte of data from a fixed/specified source to a fixed/specified destination
Mnemonic: MOV destination , source
MOV Operand 1 , Operand 2
Operation :
Destination
Operand 1
Operand 2
Source
Sr. No. | Destination | Source
1. | Memory | Accumulator
2. | Accumulator | Memory
3. | Register | Register
4. | Register | Memory
5. | Memory | Register
6. | Register | Immediate
7. | Memory | Immediate
8. | Seg-Reg | Reg – 16(GPR)
9. | Seg-Reg | Mem – 16
10. | Reg – 16(GPR) | Seg-Reg
11. | Memory | Seg-Reg
Flags :
No Flags affected

## Slide 6: MOV memory , accumulator
This instruction copies the contents of accumulator into memory location specified in the instruction
Mnemonic: MOV memory , accumulator
Operation :
memory
accumulator
Example: MOV [SI] , AL
 | 04
1023 | 
AX
BX
CX
DX
SI
DI
BP
SP
04
1023

## Slide 7: MOV register , memory
This instruction will copy the contents of the memory location specified in the instruction to the destination register
Mnemonic: MOV register , memory accumulator
Operation :
register
memory
Example: MOV CX , COUNT[DI]
Addressing mode : register relative addressing mode

## Slide 8
Example: MOV CX , COUNT[DI]
Addressing mode : register relative addressing mode
AA | 2B
1100 | 
AX
BX
CX
DX
SI
DI
BP
SP
EU
CS | 2105
DS | 2314
ES | 
SS | 
IP | 187A
228CA | Opcode of MOV instruction
228CB | 
228CC | 00
228CD | 10
228CE | 
25240 | 12
25241 | 34
BIU
Starting address (CS + IP)
CS = 21050
+ 187A
228CA
Here assuming COUNT = 1000 similar with relative addressing mode
DS = 23140
+1100
24240
+1000
25240
Example: MOV CX , [DI+1000]
Before Execution
For program :
For Data :

## Slide 9
Example: MOV CX , COUNT[DI]
Addressing mode : register relative addressing mode
12 | 34
1100 | 
AX
BX
CX
DX
SI
DI
BP
SP
EU
CS | 2105
DS | 2314
ES | 
SS | 
IP | 187E
228CA | Opcode of MOV instruction
228CB | 
228CC | 00
228CD | 10
228CE | Opcode of next instruction
25240 | 34
25241 | 12
BIU
Example: MOV CX , [DI+1000]
After Execution
CS = 21050
+ 187E
228CE

## Slide 10: PUSH Instruction
This instruction is used to transfer the contents of the specified register are copied onto the stack in the following sequences:
The stack pointer is decremented by 1 and contents of higher order register copied on that location
The stack pointer is again decremented by 1 and contents of lower order register copied on that location
Mnemonic: PUSH source
Operation :
SP = SP – 2
SS : [SP] (top of the stack)=Operand
Flags :
No Flags affected
Addressing mode : register indirect addressing mode
Register Stack

## Slide 11
Example: PUSH AX
03 | 04
2586 | 
AX
BX
CX
DX
SI
DI
BP
SP
0000
2584
2585
2586
FFFF
03
SS
SP - 2
The stack pointer is decremented by 1 and contents of higher order register copied on that location
SP - 1
SP
05 | 04
2584 | 
AX
BX
CX
DX
SI
DI
BP
SP
FFFF
2584
2585
2586
0000
04
03
SP - 1
SP
The stack pointer is again decremented by 1 and contents of lower order register copied on that location
SS
AH
AL
AH
AL
SP – 2 =SP
CS
SS
DS
ES

## Slide 12: POP Instruction
This instruction is used to transfer the contents of the stack into register the following sequences:
The stack pointer is incremented by 1 and contents of the memory location are copied into higher order
The stack pointer is again incremented by 1 and contents of the memory location are copied into lower order register
Mnemonic: POP Destination
Operation :
SP = SP + 2
SS : [SP] (top of the stack)=Operand
Flags :
No Flags affected
Addressing mode : register indirect addressing mode
Register Stack

## Slide 13
Example: POP AX
SP
 | 04
2584 | 
AX
BX
CX
DX
SI
DI
BP
SP
FFFF
2584
2585
2586
0000
04
05
SP + 1
The copy the contents of lower order register copied on that location
SS
AH
AL
05 | 04
2586 | 
AX
BX
CX
DX
SI
DI
BP
SP
0000
2584
2585
2586
FFFF
04
05
SS
The stack pointer is incremented by 1 and contents of higher order register copied on that location
SP + 1
AH
AL
SP
SP + 2
SP + 2 = SP

## Slide 14: XCHG Instruction
This instruction is used to exchange the contents of AX and BX
Mnemonic: XCHG
Operation :
Destination Source
Flags :
No Flags affected
Addressing mode : Implied addressing mode
Destination Source
For AX and BX only
NOTE :

## Slide 15: Example : XCHG AX,BX
3B | 04
01 | 02
AX
BX
CX
DX
SI
DI
BP
SP
AH
AL
01 | 02
3B | 04
AX
BX
CX
DX
SI
DI
BP
SP
AH
AL
Before Execution
After Execution

## Slide 16: XLAT / XLTAB Instruction(Translate or Replace byte)
This instruction replaces a byte in AL register with a byte from a look up table in the memory.
Here the contents of AL before execution acts as index to the desired location in lookup table.
Mostly this concept is used to convert BCD to ASCII or to seven segment.
Mnemonic: XLAT
Operation :
AL = DS :[BX + AL]
Flags :
No Flags affected
Addressing mode : Implied addressing mode
For AL and BX only
NOTE :

## Slide 17
 | 02
20 | 00
AX
BX
CX
DX
SI
DI
BP
SP
EU
CS | 2105
DS | 2314
ES | 
SS | 
IP | 187A
228CA | Opcode of XLTA instruction
228CB | 
228CC | 
228CD | 
228CE | 
25140 | 12
25141 | 34
25142 | 35
25143 | 
BIU
CS = 21050
+ 187A
228CA
DS = 23140
+2000
25140
+ 02
25142
Before Execution
After Execution
 | 35
20 | 00
AX
BX
CX
DX
SI
DI
BP
SP
EU
CS | 2105
DS | 
ES | 
SS | 
IP | 
BIU
228CA | Opcode of XLTA instruction
228CB | 
228CC | 
228CD | 
228CE | 
25140 | 12
25141 | 34
25142 | 35
25143 | 
For program :
For Data :

## Slide 18
a
b
c
d
e
f
Seven Segment Display
Cathode = 0
Anode = 1
FFFF
4000
4001
4002
4009
0’
1’(06)
2’
9’
DS
AX
BX
 | 01
40 | 00
g
. (dp)
a
b
c
d
e
f
g
0
1
1
0
0
0
0
06
dp
0
=
1’
AL = DS :[BX + AL]
Mov BX, 4000
Mov AL , 01
XLAT
To get the code of 5

## Slide 19: 3.Address Object
Address Object
LEA
LDS
LES

## Slide 20: LEA Load effective Address
This instruction determines the offset of variables or memory location named as source and puts the offset in the indicated 16 bit register.
This instruction is replaced by mov when assembly is possible.
Normally the offset is loaded into index or base pointer register such as SI,DI,BX,BP
Mnemonic: LEA AX,COUNT
Operation :
Loads AX with the offset count
AX offset of COUNT
Flags :
No Flags affected
Addressing mode : register direct addressing mode

## Slide 21
AH
AL
52 | 58
0000 | 
20 21 | 
FFFF | 
Before Execution
After Execution
AH
AL
20 | 21
0000 | 
20 21 | 
FFFF | 
AX register is used to store offset value after execution of this instruction

## Slide 22: LDS Load pointer with DS
The source is always a memory location. DS is used as a segment register for memory.
This instruction copies a word from two memory locations into register specified in instruction.
It then copies a word from the next two memory locations into the DS register.
Mnemonic: LDS reg, source
Operation :
REG = first word,
DS = Second word
Flags :
No Flags affected
Addressing mode : register direct addressing mode
Load register and DS with words from memory

## Slide 23
Reg BX
02 | 08
0000 | 
25185 | 01
25186 | 50
25187 | 23
25188 | 78
FFFF | 
Before Execution
After Execution
0000 | 
25185 | 01
25186 | 50
25187 | 23
25188 | 78
FFFF | 
CS | 2105
DS | 2314
ES | 
SS | 
IP | 
Example: LDS BX,count
Assume count = 2045
DS = 23140
+2045
25185
DS
REG = first word,
DS = Second word
Operation :
Reg BX
50 | 01
DS
CS | 2105
DS | 7823
ES | 
SS | 
IP | 

## Slide 24: LES Load pointer using ES
The source is always a memory location. DS is used as a segment register for memory.
This instruction copies a word from two memory locations into register specified in instruction.
It then copies a word from the next two memory locations into the DS register.
Mnemonic: LES reg, source
Operation :
REG = first word,
ES = Second word
Flags :
No Flags affected
Addressing mode : register direct addressing mode
Load register and ES with words from memory

## Slide 25
Reg BX
02 | 08
0000 | 
25185 | 01
25186 | 50
25187 | 23
25188 | 78
FFFF | 
Before Execution
After Execution
0000 | 
25185 | 01
25186 | 50
25187 | 23
25188 | 78
FFFF | 
CS | 2105
DS | 2314
ES | 
SS | 
IP | 
Example: LES BX,count
Assume count = 2045
DS = 23140
+2045
25185
DS
REG = first word,
ES = Second word
Operation :
Reg BX
50 | 01
DS
CS | 2105
DS | 
ES | 7823
SS | 
IP | 

## Slide 26: 4.Flag Instruction (Flag transfer)
Flag transfer
LAHF
SAHF
PUSHF
POPF

## Slide 27: LAHF Load AH reg from flags
This instruction is used to transfer lower byte of flag register into AH register
Mnemonic: LAHF
Operation :
AH = lower byte of flag register
Flags :
No Flags affected
Addressing mode : Implied addressing mode
Copy Lower byte of flag register to AH

## Slide 28
AH
AL
52 | 58
Before Execution
After Execution
Example: LAHF
0909 = 0000 1001 0000 1001
FFFF = 1111 1111 1111 1111
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
0000 1001 0000 1000
1
U
U
U
U
OF
DF
IF
TF
SF
ZF
U
AF
U
PF
U
CF
0
0
0
0
1
1
0
0
0
0
0
1
0
0
0
1
0C
11
AH
AL
11 | 58
U
U
U
U
OF
DF
IF
TF
SF
ZF
U
AF
U
PF
U
CF
0
0
0
0
1
1
0
0
0
0
0
1
0
0
0
1
0C
11

## Slide 29: SAHF Store AH reg in flags
This instruction is used to transfer content AH register into lower byte of flag register
Mnemonic: SAHF
Operation :
lower byte of flag register = AH
Flags :
No Flags affected
Addressing mode : Implied addressing mode
Copy AH into Lower byte of flag register

## Slide 30
AH
AL
03 | 58
Before Execution
After Execution
Example: SAHF
0909 = 0000 1001 0000 1001
FFFF = 1111 1111 1111 1111
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
0000 1001 0000 1000
1
U
U
U
U
OF
DF
IF
TF
SF
ZF
U
AF
U
PF
U
CF
0
0
0
0
1
1
0
0
0
0
0
1
0
0
0
1
0C
11
AH
AL
07 | 58
U
U
U
U
OF
DF
IF
TF
SF
ZF
U
AF
U
PF
U
CF
0
0
0
0
1
1
0
0
0
0
0
1
0
1
1
1
0C
07

## Slide 31: PUSHF push flags onto stack
This instruction is used to transfer flag register onto stack.
The stack pointer is decremented by 1 and contents of higher order byte of flag register copied on that location
The stack pointer is again decremented by 1 and contents of lower byte of flag order register copied on that location
Mnemonic: PUSHF
Operation :
Flags :
No Flags affected
Addressing mode : Register addressing mode
SP = SP - 2
SS : [SP] (top of the stack)=Operand

## Slide 32
Example: PUSHF
0000
2584
2585
2586
FFFF
03
SS
SP - 2
The stack pointer is decremented by 1 and contents of higher order register copied on that location
SP - 1
SP
FFFF
2584
2585
2586
0000
58
03
SP - 1
SP
The stack pointer is again decremented by 1 and contents of lower order register copied on that location
SS
Flag Register
SP – 2 =SP
03 | 58
MSB | LSB
Flag Register
03 | 58
MSB | LSB

## Slide 33: POPF Instruction
This instruction is used to transfer the contents of the stack into register the following sequences:
The stack pointer is incremented by 1 and contents of the memory location are copied into higher order byte of flag register
The stack pointer is again incremented by 1 and contents of the memory location are copied into lower order byte of flag register
Mnemonic: POPF
Operation :
SP = SP + 2
SS : [SP] (top of the stack)=Operand
Flags :
No Flags affected
Addressing mode : register addressing mode

## Slide 34
Example: POP AX
SP
FFFF
2584
2585
2586
0000
04
05
SP + 1
The stack pointer is again decremented by 1 and contents of lower order register copied on that location
SS
0000
2584
2585
2586
FFFF
04
05
SS
The stack pointer is decremented by 1 and contents of higher order register copied on that location
SP + 1
SP
SP + 2
SP + 2 = SP
Flag Register
04 | 
MSB | LSB
Flag Register
04 | 05
MSB | LSB

## Slide 35: 2. Arithmetic group
Arithmetic Group
Addition
Subtraction
Multiplication
Division
2.1
2.2
2.3
2.4
ADD
ADC
INC
DAA
AAA
SUB
SBB
DEC
NEG
CMP
DAS
AAS
MUL
IMUL
AAM
DIV
IDIV
AAD
CBW
CWD

## Slide 36: 2.1 Addition Group
Addition
ADD
ADC
INC
DAA
AAA
2.1
2.1.1
2.1.2
2.1.3
2.1.4
2.1.5

## Slide 37: 2.1.1 ADD – Add byte or word
This instruction adds a number from source to number from destination and puts the result to specified destination.
Mnemonic: ADD destination , source
ADD Operand 1 , Operand 2
Sr. No. | Destination | Source
1 | Register | Register
2 | Register | Memory
3 | Memory | Register
4 | Register | Immediate
5 | Memory | Immediate
6 | Accumulator | Immediate
Flags :
All Flags affected
Operation :
Destination
Operand 1
Operand 2
Source + Destination
Operand 1 +

## Slide 38: ADD register , register
Mnemonic: ADD register , register
Example: ADD BL, CL
This instruction adds the data in registers.
The result is stored in register. It can be 8 bit/ 16 bit instruction.
This instruction can be 8/16 bit.
Operation :
Register
Register + Register
BL
BL + CL
Addressing mode : Register addressing mode
Before execution CL = 04 , BL = 03
 | 03
 | 04
AX
BX
CX
DX
SI
DI
BP
SP
 | 07
 | 04
AX
BX
CX
DX
SI
DI
BP
SP
Before Execution
After Execution
ADD BL, CL
After execution CL = 04 , BL = 07
Flags :
All Flags affected

## Slide 39: ADD register , memory
Mnemonic: ADD register , memory
Example: ADD AX, [2000]
This instruction adds the data from memory location and required registers.
The result is stored in register.
This instruction can be 8/16 bit.
Operation :
Register
Register + content of memory location
AX
AX + content of memory location
Addressing mode : Register addressing mode
Flags :
All Flags affected

## Slide 40
02 | 03
2000 | 
AX
BX
CX
DX
SI
DI
BP
SP
EU
CS | 2105
DS | 2314
ES | 
SS | 
IP | 187A
228CA | Opcode of ADD instruction
228CB | 
228CC | 
228CD | 
228CE | 
25140 | 04
25141 | 05
25142 | 35
25143 | 
BIU
CS = 21050
+ 187A
228CA
DS = 23140
+2000
25140
Before Execution
After Execution
06 | 08
AX
BX
CX
DX
SI
DI
BP
SP
EU
CS | 2105
DS | 
ES | 
SS | 
IP | 
BIU
228CA | Opcode of ADD instruction
228CB | 
228CC | 
228CD | 
228CE | 
25140 | 04
25141 | 05
25142 | 35
25143 | 
For program :
For Data :

## Slide 41: 2.1.2 ADC – Add with carry
This instruction adds destination operand contents , source operand contents and Carry flag content.
Result is stored back to destination operand.
The source and destination can be 8/16 bit register or memory location. The source can also 8/16 bit register or memory location and immediate data.
It is easy to perform multiple – precision arithmetic by using ADC instruction.
Mnemonic: ADD destination , source
Flags :
All Flags affected
Operation :
Destination
Destination + Source + CY
1234
1234
+
2468
Two 16 bit number addition
ADD
Two 32 bit number addition
1234 8123
1234 8123
+
2469 6246
1
ADD
ADD + CY
ADC

## Slide 42: 2.1.3 INC – Increment byte or word by 1
This instruction adds 1 to the destination operand.
The operand can be a register or memory location.
The operand may be a byte or word and it is treated as an unsigned binary number.
Mnemonic: INC destination
Flags :
All Flags affected except carry flag.(carry flag not changed)
Operation :
Destination
Destination + 1
Example: INC CX
INC AL
INC [2000]
IF CX = 1234 , after INC CX will be 1235
IF AL = 08 , after INC AL will be 09
This instruction increments the content of memory location 2000 by 1.
If 2000 = 04 , after INC it will be 05

## Slide 43: 2.1.4 DAA (Decimal Adjust After Addition)
This instruction is used to changed the contents of accumulator from a binary value to its equivalent BCD number.

## Slide 44
30 h
20 h
+
50 h
24 h
24 h
+
48 h
Addition of hexadecimal numbers :
50 h
48 h
25 h
25 h
+
50 h
4A h
Expected answer
Actual answer
28 h
27 h
+
55 h
4F h
28 h
28 h
+
56h
50 h
Case 1 :
50 h
50 h
+
100 h
64 h
54h
+
118 h
A0 h
B8 h
Expected answer
Actual answer
Case 2 :
84 h
94h
+
168 h
108 h
88 h
88 h
+
176 h
110 h
Expected answer
Actual answer
Case 3 :
There is a gap of 6 numbers

## Slide 45
Decimal | BCD | Hexadecimal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 0001 0000 | A
11 | 0001 0001 | B
12 | 0001 0010 | C
13 | 0001 0011 | D
14 | 0001 0100 | E
15 | 0001 0101 | F
16 | 0001 0110 | 10
17 | 0001 0111 | 11
Up to 9 numbers BCD and HEX numbers are same
From 10 to 15 in HEX , 6 Characters are used and after these 6 characters 10 onwards numbers are started.
So there is a 6 characters gap between BCD and hex

## Slide 46: 2.1.4 DAA (Decimal Adjust After Addition)
This instruction is used to changed the contents of accumulator from a binary value to its equivalent BCD number.
Working of DAA instruction :
AL
HN
LN
If higher nibble is > 9 II Carry flag = 1 then
add 60
If lower nibble is > 9 II Auxiliary flag = 1 then
add 06
0
1
1
0
0
0
0
60/06
0
higher nibble
lower nibble
Why 6 is added?
Addressing mode : Implied
Mnemonic: DAA
Flags :
AF,CF,PF,ZF and SF

## Slide 47
Decimal | BCD | Hexadecimal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 0001 0000 | A
11 | 0001 0001 | B
12 | 0001 0010 | C
13 | 0001 0011 | D
14 | 0001 0100 | E
15 | 0001 0101 | F
16 | 0001 0110 | 10
17 | 0001 0111 | 11
Up to 9 numbers BCD and HEX numbers are same
From 10 to 15 in HEX , 6 Characters are used and after these 6 characters 10 onwards numbers are started.
So there is a 6 characters gap between BCD and hex and to overcome this gap 6 is added
Why 6 is added?

## Slide 48
30 h
20 h
+
50 h
24 h
24 h
+
48 h
Addition of hexadecimal numbers :
50 h
48 h
25 h
25 h
+
50 h
4A h
Expected answer
Actual answer
28 h
27 h
+
55 h
4F h
28 h
28 h
+
56h
50 h
Case 1 :
50 h
50 h
+
100 h
64 h
54h
+
118 h
A0 h
B8 h
Expected answer
Actual answer
Case 2 :
84 h
94h
+
168 h
108 h
88 h
88 h
+
176 h
110 h
Expected answer
Actual answer
Case 3 :
There is a gap of 6 numbers

## Slide 49
Case 1 : (for lower nibble)
AL
HN
LN
If higher nibble is > 9 I I Carry flag = 1 then
add 60
If lower nibble is > 9 I I Auxiliary flag = 1 then
add 06
Rule :
30 h
20 h
+
50 h
LN is not > 9 , Auxiliary flag = 0
Therefore , output same
a) Both conditions not true
25 h
25 h
+
4A h
LN > 9 , Auxiliary flag = 0
Therefore add 06 into LN
0010 0101
0010 0101
+
0000 0110
+
0100 1010
4A h
06 h
0101 0000
50 h
b) one conditions true i.e. LN > 9
28 h
28 h
+
50 h
LN > 9 & Auxiliary flag = 1
Therefore add 06 into LN
0010 1000
0010 1000
+
0000 0110
+
0101 0000
50 h
06 h
0101 0110
56 h
1
c) one conditions are true i.e. Ln>! 9 and AF = 1
Back

## Slide 50
Case 2 : (for higher nibble)
AL
HN
LN
If higher nibble is > 9 && Carry flag = 1 then
add 60
If lower nibble is > 9 && Auxiliary flag = 1 then
add 06
Rule :
30 h
20 h
+
50 h
HN is not > 9 , Carry flag = 0
Therefore , output same
a) Both conditions not true
50 h
50 h
+
A0 h
HN > 9 , Carry flag = 0
Therefore add 06 into LN
0101 0000
0101 0000
+
0110 0000
+
1010 0000
A0 h
60 h
0000 0000
100 h
b) one conditions true i.e. LN > 9
84 h
94 h
+
108 h
HN >9 & Carry flag = 1
Therefore add 06 into LN
1000 0100
1001 0100
+
0110 0000
+
0001 1000
108 h
60 h
0111 1000
178 h
c) both conditions are true i.e. HN> 9 and CF = 1
1
1
Prev carry
1
Back

## Slide 51
Case 3 : (for both nibble)
AL
HN
LN
If higher nibble is > 9 || Carry flag = 1 then
add 60
If lower nibble is > 9 || Auxiliary flag = 1 then
add 06
Rule :
88 h
88 h
+
108 h
1000 1000
1000 1000
+
0110 0110
+
0001 0000
100 h
66 h
0111 0110
176 h
both conditions are true i.e. HN/LN > 9 and CF/AF = 1
1
1
Prev carry
1

## Slide 52: AAA Instruction

## Slide 53
ASCII
34
Packed BCD
34
0011 0100
Unpacked BCD
34
0000 0100
03
04
0000 0011
0000 0100

## Slide 54
ASCII Input (keyboard)
Unpacked BCD format
Binary format
Binary format
Unpacked BCD format
ASCII output (monitor)
Conversion
Conversion
Computer follows ASCII input and
output.
We get from keyboard ASCII character
and we have to send out ASCII character
to monitor. Therefore we have to convert
ASCII to binary

## Slide 55: ASCII code for digit 0-9
Key | ASCII (hex) | BCD (unpacked)
0 | 30 | 0011 0000
1 | 31 | 0011 0001
2 | 32 | 0011 0010
3 | 33 | 0011 0011
4 | 34 | 0011 0100
5 | 35 | 0011 0101
6 | 36 | 0011 0110
7 | 37 | 0011 0111
8 | 38 | 0011 1000
9 | 39 | 0011 1001

## Slide 56: AAA (ASCII Adjust after addition)
Numerical data coming into a computer from a terminal through keyboard is usually in ASCII code.
The numbers 0 to 9 are represented by ASCII codes 30H to 39H .
The 8086 allows to add the ASCII codes for two decimal digits without masking off “3” in the upper nibble for each.
After addition , AAA instruction is used to make sure that the result is the correct unpacked BCD
The AAA instruction works only AL register.
Mnemonic: AAA
Operation :
Flags :
AF and CF flags are changed
Addressing mode : Implied
AL
HN
LN
If lower nibble is > 9
add 06
Clear higher nibble &
add 01 (carry)

## Slide 57
AL = 0011 0101(ASCII 5)
BL = 0011 1001(ASCII 9)
Rule :
AL
HN
LN
If lower nibble is > 9
add 06
Clear higher nibble &
add 01 (carry)
35 h
39 h
+
6E h
0011 0101
0011 1001
+
0110
+
0110 1110
Add 6
0000 0100
1 11
Clear HN
carry
+
1
0001 0100
14 h

## Slide 58: 2.2 Subtraction Group
Subtraction
SUB
SBB
DEC
DAS
AAS
2.2
2.2.1
2.2.2
2.2.3
2.2.4
2.2.5
CMP
2.2.6
NEG
2.2.7

## Slide 59: 2.1.1 SUB – Subtract byte or word
This instruction subtracts a number from source to number from destination and puts the result to specified destination.
Mnemonic: SUB destination , source
SUB Operand 1 , Operand 2
Sr. No. | Destination | Source
1 | Register | Register
2 | Register | Memory
3 | Memory | Register
4 | Register | Immediate
5 | Memory | Immediate
6 | Accumulator | Immediate
Flags :
All Flags affected
Operation :
Destination
Operand 1
Operand 2
Destination - Source
Operand 1 -

## Slide 60: SUB register , register
Mnemonic: SUB register , register
Example: SUB BL, CL
This instruction subtracts the data in registers.
The result is stored in register.
This instruction can be 8/16 bit.
Operation :
Register
Register - Register
BL
BL - CL
Addressing mode : Register addressing mode
Before execution CL = 02 , BL = 05
 | 05
 | 02
AX
BX
CX
DX
SI
DI
BP
SP
 | 03
 | 02
AX
BX
CX
DX
SI
DI
BP
SP
Before Execution
After Execution
SUB BL, CL
After execution CL = 04 , BL = 07
Flags :
All Flags affected

## Slide 61: 2.2.2 SBB – Subtract with borrow
This instruction subtracts destination operand contents , source operand contents and Carry flag content.
Result is stored back to destination operand.
The source and destination can be 8/16 bit register or memory location. The source can also 8/16 bit register or memory location and immediate data.
It is easy to perform multiple – precision arithmetic by using SBB instruction.
Mnemonic: SBB destination , source
Flags :
All Flags affected
Operation :
Destination
Destination - Source - CY
Example: SBB BL, CL

## Slide 62: 2.2.3 DEC – Decrement byte or word by 1
This instruction subtracts 1 from the destination operand.
The operand can be a register or memory location.
The operand may be a byte or word and it is treated as an unsigned binary number.
Mnemonic: DEC destination
Flags :
All Flags affected except carry flag.(carry flag not changed)
Operation :
Destination
Destination - 1
Example: DEC CX
DEC AL
DEC [2000]
IF CX = 1234 , after DEC CX will be 1233
IF AL = 08 , after DEC AL will be 07
This instruction decrements the content of memory location 2000 by 1.
If 2000 = 04 , after DEC it will be 04

## Slide 63: 2.2.6 CMP –Compare byte or word
This instruction compares a word/byte from source with byte/word from destination.
The comparison is done by subtracting the source byte or word from the destination byte or word.
The result is not stored in either of the destination or source.
The destination and source remain unchanged, only flags are updated.
Mnemonic: CMP Destination , Source
Flags :
AF, OF, SF, ZF, PF are updated
Operation :
Destination - source
Compare | CF | ZF | SF | 
Source > Destination | 1 | 0 | 1 | Subtraction required borrow, CF =1
Source < Destination | 0 | 0 | 0 | No borrow required, CF =0
Source = Destination | 0 | 1 | 0 | Result of subtraction is zero.
******* After each operation in this instruction carry flag changed……
if 0 then it will become 1
if 1 then it will become 0

## Slide 64
Example1:
CMP BL, CL
Where, BL = 05 , CL = 04
05 = 0 0 0 0 0 1 0 1 : BL
04 = 0 0 0 0 0 1 0 0 : CL
05 h
04 h
-
+
05 = 0 0 0 0 0 1 0 1
- 04 = 1 1 1 1 1 1 0 0
04 = 0 0 0 0 0 1 0 0
1 1 1 1 1 0 1 1
+ 1
2’s Complement
1 1 1 1 1 1 0 0
- 04 =
CY = 1
+
0 0 0 0 0 0 0 1
CY = 0
Carry changed
1
1
1
1
1
1
Carry changed
0
Compare | CF | ZF | SF | 
Source > Destination | 1 | 0 | 1 | Subtraction required borrow, CF =1
Source < Destination | 0 | 0 | 0 | No borrow required, CF =0
Source = Destination | 0 | 1 | 0 | Result of subtraction is zero.
Where, BL = 08 , BL = 03

## Slide 65
Example:
CMP BL, CL
Where, BL = 04 , CL = 05
05 = 0 0 0 0 0 1 0 1 : CL
04 = 0 0 0 0 0 1 0 0 : BL
04 h
05 h
-
+
04 = 0 0 0 0 0 1 0 0
- 05 = 1 1 1 1 1 0 1 1
05 = 0 0 0 0 0 1 0 1
1 1 1 1 1 0 1 0
+ 1
2’s Complement
1 1 1 1 1 0 1 1
- 05 =
CY = 1
+
1 1 1 1 1 1 1 1
CY = 1
1’s Complement
Carry changed
0
0
Carry changed
Compare | CF | ZF | SF | 
Source > Destination | 1 | 0 | 1 | Subtraction required borrow, CF =1
Source < Destination | 0 | 0 | 0 | No borrow required, CF =0
Source = Destination | 0 | 1 | 0 | Result of subtraction is zero.
Where, BL = 04 , BL = 06

## Slide 66
Example:
CMP BL, CL
Where, BL = 05 , CL = 05
05 = 0 0 0 0 0 1 0 1 : CL
05 = 0 0 0 0 0 1 0 1 : BL
05 h
05 h
-
+
05 = 0 0 0 0 0 1 0 1
- 05 = 1 1 1 1 1 0 1 1
05 = 0 0 0 0 0 1 0 1
1 1 1 1 1 0 1 0
+ 1
2’s Complement
1 1 1 1 1 0 1 1
- 05 =
CY = 1
+
0 0 0 0 0 0 0 0
CY = 0
1’s Complement
Carry changed
0
1
Carry changed
Compare | CF | ZF | SF | 
Source > Destination | 1 | 0 | 1 | Subtraction required borrow, CF =1
Source < Destination | 0 | 0 | 0 | No borrow required, CF =0
Source = Destination | 0 | 1 | 0 | Result of subtraction is zero.
Where, BL = 07 , CL = 07

## Slide 67: 2.2.7 NEG –Negate byte or word
This instruction replace the number is a destination with 2’s complement of that number.
The destination can be register or memory.
Mnemonic: NEG Destination
Flags :
All flags are updated
Operation :
Destination
2’s complement of Destination
Example: NEG BL
BL
2’s complement of BL
Before execution BL = 05
 | 05
AX
BX
CX
DX
SI
DI
BP
SP
 | FB
AX
BX
CX
DX
SI
DI
BP
SP
Before Execution
After Execution
NEG BL
After execution BL = FB

## Slide 68: 2.3 Multiplication Group
Multiplication
MUL
IMUL
AAM
2.3
2.3.1
2.3.2
2.3.3

## Slide 69: 2.3.1 MUL – Multiply byte or word unsigned
This instruction multiplies an unsigned byte from source with an byte in the AL register or an unsigned word from source with an unsigned word in AX.
When a byte is multiplied by contents of AL, the result is stored in AX.
The MSB of result is stored in AH register and the LSB of result is stored in the AL register.
When a word is multiplied by contents of AX, then MSB of result is stored in DX register and the LSB of result is stored in the DX register.
Mnemonic: MUL multiplier
Flags :
AF,PF,SF,ZF undefined
CF and OF will both be 0
Operation :
AX
Multiplication
MSB
AH
LSB
AL
Example: MUL BL
Where AL = 09 H,
BL = 02 H
09 h
02 h
X
0012 h
AH = 00 H
AL = 12 H

## Slide 70: 2.4 Division Group
Division
DIV
IDIV
2.4
2.4.1
2.4.2

## Slide 71: 2.4.1 DIV – Multiply byte or word unsigned
This instruction divides an unsigned byte from source with an byte in the AL register or an unsigned word from source with an unsigned word in AX.
When a byte is divided , the result is stored in AX.
The remainder of result is stored in AH register and quotient of result is stored in the AL register.
For 16 bit operation DX register is used.
Mnemonic: DIV Divider
Operation :
AX
Division
Rem
AH
Quo
AL
Example: DIV BL
Where AL = 08 H,
BL = 02 H
08 h
02 h
/
04 h
AH = remainder
AL = quotient
Q