## Slide 1: Processor control Instructions of 8086

## Slide 2
Processor Control Instructions
Flag Operations
No Operation
External synchronization
STC
CLC
CMC
STD
CLD
STI
CLI
NOP
HLT
WAIT
ESC
LOCK

## Slide 3
STC – Set Carry Flag
Mnemonic: STC
This instruction is used to set the carry flag.
Operation :
Example:
STC
CF = 1
Flag Operations
Addressing Mode : Implied addressing mode
Flags : Except carry flag no other flags are affected.
1
U
U
U
U
OF
DF
IF
TF
SF
ZF
U
AF
U
PF
U
CF

## Slide 4
CLC – Clear Carry Flag
Mnemonic: CLC
This instruction is used to clear the carry flag.
Operation :
Example:
CLC
CF = 0
Addressing Mode : Implied addressing mode
Flags : Except carry flag no other flags are affected.
0
U
U
U
U
OF
DF
IF
TF
SF
ZF
U
AF
U
PF
U
CF

## Slide 5
CMC – Complement Carry Flag
Mnemonic: CMC
This instruction is used to complement the carry flag.
Operation :
Example:
CMC
CF = CF
Addressing Mode : Implied addressing mode
Flags : Except carry flag no other flags are affected.
0
U
U
U
U
OF
DF
IF
TF
SF
ZF
U
AF
U
PF
U
CF
If CF = 0 then after execution of CMC instruction CF = 1
If CF = 1 then after execution of CMC instruction CF = 0
1
1
0

## Slide 6
STD – Set Direction Flag
Mnemonic: STD
This instruction is used to set the direction flag.
DF flag is used in string instruction.
If DF= 1 then in case of string instructions SI and DI automatically decremented.
Operation :
Example:
STD
DF = 1
Addressing Mode : Implied addressing mode
Flags : Except Direction flag no other flags are affected.
U
U
U
U
OF
DF
IF
TF
SF
ZF
U
AF
U
PF
U
CF
1

## Slide 7
CTD – Clear Direction Flag
Mnemonic: CTD
This instruction is used to clear the direction flag.
DF flag is used in string instruction.
If DF= 0 then in case of string instructions SI and DI automatically incremented.
Operation :
Example:
CTD
DF = 0
Addressing Mode : Implied addressing mode
Flags : Except Direction flag no other flags are affected.
U
U
U
U
OF
DF
IF
TF
SF
ZF
U
AF
U
PF
U
CF
0

## Slide 8
STI – Set Interrupt Enable Flag
Mnemonic: STI
This instruction sets the interrupt flag to 1.
This enables INTR interrupt of the 8086.
Operation :
Example:
STI
IF = 1
Addressing Mode : Implied addressing mode
Flags : Except Interrupt flag no other flags are affected.
U
U
U
U
OF
DF
IF
TF
SF
ZF
U
AF
U
PF
U
CF
1

## Slide 9
CLI – Clear Interrupt Enable Flag
Mnemonic: CTI
This instruction resets the interrupt flag to zero.
If the interrupt flag is reset, the 8086 will not respond to an interrupt signal on its INTR input.
Operation :
Example:
STI
IF = 0
Addressing Mode : Implied addressing mode
Flags : Except Interrupt flag no other flags are affected.
U
U
U
U
OF
DF
IF
TF
SF
ZF
U
AF
U
PF
U
CF
0

## Slide 10
NOP – No Operation
Mnemonic: NOP
The execution of this instruction causes the CPU to do nothing.
This instruction uses three clock cycles and increments the instruction pointer to point to the next instruction.
It can be used to increase the delay of delay loop.
Operation :
Example: NOP
Do nothing
No Operations
Addressing Mode : Implied addressing mode
Flags : Dose not affect any flag.

## Slide 11
Mnemonic: HLT
External synchronization
Addressing Mode : Implied addressing mode
Flags : Dose not affect any flag.
HALT – Halt until interrupt or reset

## Slide 12
Mnemonic: WAIT
Addressing Mode : Implied addressing mode
Flags : Dose not affect any flag.
WAIT – Wait for test pin active

## Slide 14
when