## Slide 1: Program Transfer Group
JMP
CALL
INT

## Slide 2: Jump Instruction
Conditional Jump
Unconditional Jump
JMP

## Slide 3
JMP instruction of 8086 :
1000
JMP address (5000)
5000
---------
IP
Initially IP pointed to the memory location 1000 (before jump instruction)
IP
After execution of jump instruction IP pointed to the memory location 5000 which is new address
Unconditional Jump

## Slide 4
JMP
Syntax : JMP addr
1000
JMP 5000
5000
---------
IP
IP
0000
FFFF
PC = 5000
This is all about Theory part

## Slide 5
Practically :
JMP DOWN (label)
DOWN
Assembler will substitute this address.
Note:
As a programmer we don’t know the physical address, because we are not writing program in memory, so assembler will responsible to convert symbols or labels into a physical address.

## Slide 6: JMP– Jump to specified address:
This instruction will cause the 8086 to fetch its next instruction from the location specified in the instruction rather than from next location after JMP instruction.
There are two basic types of JMP, Near and Far
Mnemonic: JMP address
Flags :
No Flags are affected
Operation :
Jump to specified address
Example: JMP

## Slide 7
Memory
00000
FFFFF
CS
IP
DS
SI
Extra
DI
Ss
SP
CS
IP
NEAR JMP
FAR JMP
NEAR JMP | FAR JMP
Destination location is in the same segment. | Destination location is in the different segment.
When NEAR JMP only IP changed and CS will remains same. | When Far JMP then both IP and CS changed.
Less stack memory is required | More stack memory is required
It is also called as an INTRA segment JMP | It is also called as an INTER segment JMP
Near JMP and Far JMP further described as direct and indirect. If the destination address is specified within instruction it is called as direct and if the destination address is in register or memory location

## Slide 8
Conditional Jump :
Conditional transfer instructions are also called as conditional jumps instructions.
There are total 18 conditional jump instruction as per given in the table.
For conditional jump instructions, if condition is true then only control is transferred to the target specified in the instruction.
if condition is false then control is transferred to the instruction that follows the conditional JMP.
1000
Conditional JMP DOWN
DOWN
5000
---------
IP
Initially IP pointed to the memory location 1000 (before jump instruction)
IP
After execution of jump instruction IP pointed to the memory location 5000 which is new address
1002
Next Instruction
If condition = true
If condition = False

## Slide 11
 | Mov al , 00h | AL= 00
 | Mov bl, 01h | BL = 01
 | Mov cl, 05h | CL = 05
BACK : | Add al , bl | AL= 00+01 = 01
 | Dec CL | CL=05-01=04
 | Jnz BACK | ZF=0,non zero Condition is true then jump to Back
 | End | 
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
0
jump to Back
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
1
Execute next instruction

## Slide 12
CALL
Syntax : JMP addr
1000
CALL 5000
5000
---------
IP
IP
0000
FFFF
PC = 5000
This is all about Theory part
1002
PUSH
Stack
RET
POP