## Slide 1: Rotate and Shift Instructions

## Slide 2
Difference between rotate and shift
Rotate: It is a circular movement
Shift: It is a horizontal movement
No bit loss
bit loss

## Slide 3
Rotate Instructions:
ROL : Rotate bits to left
ROR : Rotate bits to right
RCL : Rotate bits to left along with carry
RCR : Rotate bits to right along with carry
NOTE :
Always CL reg is used to store the count value for rotation
If count is 01 then directly used along with instruction i.e. ROL BL, 01h
If count is other than 01 then CL reg is used to store the count value
MOV CL, 04h
ROL BL, CL
example :
MOV CL, 04h
ROL BX, CL
example :
CL is sufficient for both 8 bit as well as 16 bit data because maximum 8 bit rotation is 8 times and for 16 bit 16 times

## Slide 4
ROL : Rotate bits to left
Mnemonic: ROL destination , Count
1. This instruction is used to rotate 8 bits and 16 bits to the left.
2. MSB moves into the LSB
3. MSB also copies into the carry flag
Operation :
D7
D6
D5
D4
D3
D2
D1
CF
D0
LSB
MSB
Example:
MOV CL, 01h
ROL BL, CL
1
0
0
0
1
0
0
0
0
CF
LSB
MSB
Before Execution BL= 88 h
After Execution BL= 11 h
CF
LSB
MSB
0
0
0
1
0
0
0
1
0
1

## Slide 5
2. ROR : Rotate bits to right
Mnemonic: ROR destination , Count
1. This instruction is used to rotate 8 bits and 16 bits to the right.
2. LSB moves into the MSB
3. LSB also copies into the carry flag
Operation :
Example:
MOV CL, 01h
ROR BL, CL
1
0
0
0
1
0
0
0
0
CF
LSB
MSB
Before Execution BL= 88 h
After Execution BL= 44 h
CF
LSB
MSB
0
0
0
1
0
0
0
1
1
0
D7
D6
D5
D4
D3
D2
D1
CF
D0
LSB
MSB

## Slide 6
3. RCL : Rotate bits to left with carry
Mnemonic: RCL destination , Count
1. This instruction is used to rotate 8 bits and 16 bits to the left along with carry
2. LSB moves into the carry flag
3. Previous carry flag moves into the LSB
Operation :
D7
D6
D5
D4
D3
D2
D1
CF
D0
LSB
MSB
Example:
MOVE CL, 01h
RCL BL, CL
1
0
0
0
1
0
0
0
0
CF
LSB
MSB
Before Execution BL= 88 h
After Execution BL= 10 h
CF
LSB
MSB
0
0
0
1
0
0
0
1
0

## Slide 7
4. RCR : Rotate bits to right with carry
Mnemonic: RCR destination , Count
1. This instruction is used to rotate 8 bits and 16 bits to the right.
2. LSB moves into the MSB
3. LSB also copies into the carry flag
Operation :
Example:
MOVE CL, 01h
ROR BL, CL
1
0
0
0
1
0
0
0
0
CF
LSB
MSB
Before Execution BL= 88 h
After Execution BL= C4 h
CF
LSB
MSB
0
0
0
1
0
0
0
1
1
D7
D6
D5
D4
D3
D2
D1
CF
D0
LSB
MSB

## Slide 8
Shift Instructions:
SHL/SAL : Shift bits to left
SHR : Shift bits to right
SAR : Shift arithmetic right
NOTE :
Always CL reg is used to store the count value for shifting
If count is 01 then directly used along with instruction i.e. SHL BL, 01h
If count is other than 01 then CL reg is used to store the count value
MOV CL, 04h
SHL BL, CL
example :
MOV CL, 04h
SHL BX, CL
example :
CL is sufficient for both 8 bit as well as 16 bit data because maximum 8 bit rotation is 8 times and for 16 bit 16 times

## Slide 9
SHL/SAL : Shift bits to left
Mnemonic: SHL/SAL destination , Count
1. This instruction is used to shift 8 bits and 16 bits to the left.
2. MSB shifted into the carry.
3. LSB gets a 0.
Operation :
D7
D6
D5
D4
D3
D2
D1
CF
D0
LSB
MSB
Example:
MOV BL, 88 h
MOV CL,01h
SHL BL, CL
1
0
0
0
1
0
0
0
0
CF
LSB
MSB
Before Execution BL= 88 h
After Execution BL= 10 h
CF
LSB
MSB
0
0
0
1
0
0
0
1
0
0
0

## Slide 10
2. SHR : Shift bits to right
Mnemonic: SHR destination , Count
1. This instruction is used to shift 8 bits and 16 bits to the right.
2. LSB shifted into carry flag.
3. MSB gets 0.
Operation :
Example:
MOVE CL, 01h
SHR BL, CL
1
0
0
0
1
0
0
0
0
CF
LSB
MSB
Before Execution BL= 88 h
After Execution BL= 44 h
CF
LSB
MSB
0
0
0
1
0
0
0
1
1
D7
D6
D5
D4
D3
D2
D1
CF
D0
LSB
MSB
0
0
By putting 0 in MSB, going to change the sign of number i.e. makes the no. +ve
Hence this instruction numbers are assumed to be unsigned
If we don’t want to change the sign of number which means if +ve then +ve and if –ve then –ve (signed numbers) then use next shift instruction.

## Slide 11
3. SAR : Shift Arithmetic right
Mnemonic: SAR destination , Count
1. This instruction is used to shift 8 bits and 16 bits to the right.
2. LSB shifted into carry flag.
3. Retain and shift the MSB
Operation :
Example:
MOVE CL, 01h
SHR BL, CL
1
0
0
0
1
0
0
0
0
CF
LSB
MSB
Before Execution BL= 88 h
After Execution BL= 44 h
CF
LSB
MSB
0
0
0
1
0
0
0
1
1
D7
D6
D5
D4
D3
D2
D1
CF
D0
LSB
MSB
1
1
Number will become -ve
0
Number will become +ve
MSB is retained as well as shifted