## Slide 1
String Instructions
Why string instructions are used????
When we want to perform operations on block of data with speed then string instructions are used.
04
45
20
05
65
02
89
45
Example : there are two blocks , block 1 and block2. Block 1 having elements and block 2 is empty. We want to copy block 1 data into block 2
Block 1
Block 2
There are two methods
Without String instruction
Using String instruction
Use SI pointer to point Block 1 (source data)
SI
Move first element into any reg.
MOV BL , [SI]
Use DI pointer to point Block 2 (destination data)
DI
Transfer first element from reg to destination block
MOV [DI] , BL
04
Increment both pointer by 1 to point next location
INC SI
INC DI
SI+1
DI+1
Repeat above steps till data transfer overs, so need to execute loop.
Use specific single string instruction to perform given transfer
Less number of coding required
Suitable for large number of data
Data operation speed is fast as compare to manual data transfer

## Slide 2
String Instructions
MOVS
LODS
CMPS
SCANS
STOS
Key Points for string instructions:
1. SI - Index offset for source string
2. DI - Index offset for destination string
3. CX - Default counter register
4. AL/AX – Register which required to stored data for string instructions.
5. CLD - clear direction flag (DF = 0)
6. SLD – Set direction flag. (DF= 1)
DF = 0 : Auto increment SI,DI pointers
DF = 1 : Auto decrement SI,DI pointers
Prefix used with string instructions:
REP – Repeat
REPE – Repeat if equal
REPNE – Repeat if not equal

## Slide 3
MOVS B/W/D :
This instruction is used to transfer the contents of source to destination.
Operation : ES: [DI]  DS: [SI]
Types :
1. MOVSB : Moves 8 bit content of source to destination : SI = SI +1 and DI = DI + 1 if DF =0
SI = SI -1 and DI = DI - 1 if DF =1
2. MOVSW : Moves 16 bit content of source to destination : SI = SI +2 and DI = DI + 2 if DF =0
SI = SI - 2 and DI = DI - 2 if DF =1
3. MOVSD : Moves 32 bit content of source to destination : SI = SI +4 and DI = DI + 4 if DF =0
SI = SI - 4 and DI = DI - 4 if DF =1

## Slide 4
LODS B/W/D :
This instruction is used to load string byte into AL and string word into AX register. This instruction copies a byte or word from a string location pointed by SI into the AL/AX register.
Operation : AL  DS: [SI]
Types :
1. LODSB : Load 8 bit content of AL from source : SI = SI +1 if DF =0
SI = SI -1 if DF =1
2. LODSW : Load 16 bit content of AX from source : SI = SI +2 if DF =0
SI = SI - 2 if DF =1
3. LODSD : Load 32 bit content of EAX from source : SI = SI +4 if DF =0
SI = SI - 4 if DF =1
AL  DS: [SI]
AX  DS: [SI]
EAX  DS: [SI] (80386)

## Slide 5
STOS B/W/D :
This instruction is used to load string byte from AL and string word from AX register. This instruction copies a byte or word from a AL/AX reg into string location pointed by DI in extra segment.
Operation : AL  ES: [DI]
Types :
1. STOSB : Store 8 bit content of AL into destination : DI = DI + 1 if DF =0
DI = DI - 1 if DF =1
2. STOSW : Store 16 bit content of AX into destination : DI = DI + 2 if DF =0
DI = DI - 2 if DF =1
3. STOSD : Store 32 bit content of EAX into destination : DI = DI + 4 if DF =0
DI = DI - 4 if DF =1
AL  ES: [DI]
AX  ES: [DI]
EAX  DS: [DI] (80386)

## Slide 6
SCAS B/W/D :
This instruction is used to compare a byte/word into AL/AX with a byte pointed by DI in ES.
Operation : Compare AL/AX with ES: [DI]
Types :
1. SCASB : Compare 8 bit content of AL with destination : DI = DI + 1 if DF =0
DI = DI - 1 if DF =1
2. SCASW : Compare 16 bit content of AX with destination : DI = DI + 2 if DF =0
DI = DI - 2 if DF =1
3. SCASD : Compare 32 bit content of EAX with destination : DI = DI + 4 if DF =0
DI = DI - 4 if DF =1

## Slide 7
.model small
.data
arr db 80 dup(?)
.code
lea di,arr
mov al, ODh
mov CX, 80
CLD
Repne scasb
WAP to find the displacement at which the data 0DH is present from an array of data stored from location ‘Arr’, the no. of bytes of data in the array is 80.
For this there are two ways to exit :
If match is found
If match not found and CX=0

## Slide 8
CMPS B/W/D :
This instruction is used to compare a byte/word into source string of DS pointed by SI with a byte/word pointed by DI in ES.
Operation : Compare DS:[SI] with ES: [DI]
Types :
1. CMPSB : Compare 8 bit content of source with destination : SI = SI +1 and DI = DI + 1 if DF =0
SI = SI -1 and DI = DI - 1 if DF =1
2. CMPSW : Compare 16 bit content of source with destination : SI = SI +1 and DI = DI + 1 if DF =0
SI = SI -1 and DI = DI - 1 if DF =1
3. CMPSD : Compare 32 bit content of source with destination : SI = SI +1 and DI = DI + 1 if DF =0
SI = SI -1 and DI = DI - 1 if DF =1

## Slide 9
DS:[SI] | Source | ES:[DI] | Destination
1000 | 67 | 2000 | 67
1001 | 56 | 2001 | 56
1002 | 0E | 2002 | 0E
1003 | 89 | 2003 | 89
1004 | A0 | 2004 | A0
1005 | 12 | 2005 | 41---12
.model small
.data
Src db 06 dup(?)
Des db 06 dup(?)
.code
lea Si,Src
lea Di,Des
mov CX, 06
CLD
Repe cmpsb

## Slide 10
Transfer one array into another empty array without using string instruction

## Slide 11
Take first element of an array e
mov ch, 05h
Back: mov al,[si]
inc si
mov [di],al
inc di
dec ch
jnz back
lea di,e
mov dh,05h
mov dl,' '
mov ah,02h
int 21h
inc di
dec dh
jnz back1
mov ah,4ch
int 21h
end
.model small
.data
a db 04,02,03,05,06h
e db 05 dup(?)
array with elements
Blank array to store 5 elements
.code
mov ax,@data
mov ds,ax
lea si,a
mov es,ax
lea di,e
Initialization of data segment as a source and assign SI for array a.
Initialization of data segment as a destination and assign DI for array e.
Count value to transfer elements from array a to array e
This loop is used to perform transfer from array a to array e
Point first element of array e to print
Count value to print elements
back1: mov al,[di]
mov ch,02h
mov cl,04h
mov bh, al
i2: rol bh,cl
mov dl,bh
and dl,0fh
cmp dl,09h
jbe i4
add dl,07h
i4: add dl,30h
mov ah,02h
int 21h
dec ch
jnz i2
To print first number from array
To assign space between two digits

## Slide 12
Transfer one array into another empty array using string instruction

## Slide 13
Take first element of an array e
mov ch, 05h
CLD
Rep movsb
lea si,e
mov dh, 05h
mov dl,' '
mov ah,02h
int 21h
inc si
dec dh
jnz back
mov ah,4ch
int 21h
end
.model small
.data
a db 04,02,03,05,06h
e db 05 dup(?)
array with elements
Blank array to store 5 elements
.code
mov ax,@data
mov ds,ax
lea si,a
mov es,ax
lea di,e
Initialization of data segment as a source and assign SI for array a.
Initialization of data segment as a destination and assign DI for array e.
Count value to transfer elements from array a to array e
Movsb is used to transfer 8bit data of AL reg from source to destination. Repeat this until CH =00 h
Point first element of array e to print
Count value to print elements
back: mov al,[si]
mov ch,02h
mov cl,04h
mov bh, al
i2: rol bh,cl
mov dl,bh
and dl,0fh
cmp dl,09h
jbe i4
add dl,07h
i4: add dl,30h
mov ah,02h
int 21h
dec ch
jnz i2
To print first number from array
To assign space between two digits
Clear DF for auto increment of SI & DI