## Slide 1: Flag Register of 8086

## Slide 2
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
Flag register is a part of Execution Unit.
It is a 16-bit register with each bit corresponding to a flip-flop.
Flag register is used to give status of operation performed by processor.
A flag is flip-flop.
It indicates some condition produced by the execution of an instruction.
Flag Register of 8086
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
8085 compatible flags
U = Undefined
Carry Flag
1 = Set
0= Reset
Parity Flag
1 = Set
0= Reset
Auxiliary Flag
1 = Set
0= Reset
Zero Flag
If result 0 (all zero) = Set (1)
If result is non 0 = Reset (0)
Sign Flag
Positive = 0
Negative = 1
Trap Flag
ON = 1
OFF = 0
Interrupt Flag
Interrupt Enabled = 1
Interrupt Disabled = 0
Direction Flag
Up = 1
Down= 0
Overflow Flag
Overflow = 1
No overflow= 0

## Slide 3
Carry Flag (CF)
It can also be called as a final carry.
This flag is set whenever there has been a carry out of, or borrow into, the MSB of the result (8 bit / 16 bit).
The flag is used by the instruction that add and subtract multibyte numbers.
CF = 1 , if there is a carry out from the most significant bit (MSB)
CF = 0 , if no carry out from MSB
83 h =
81 h =
+
1 0 0 0 0 0 1 1
1 0 0 0 0 0 0 1
0 0 0 0 0 1 0 0
Example 2 (8 bit) :
ADD BL, CL where BL = 83 H and CL= 81 H
BL =
CL =
Example 1 (8 bit) :
ADD BL, CL where BL = 02 H and CL= 51 H
02 h =
51 h =
+
0 0 0 0 0 0 1 0
0 1 0 1 0 0 0 1
0 1 0 1 0 0 1 1
BL =
CL =
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
MSB
LSB
Carry is not generated from MSB
0
1
1
1
MSB
LSB
Carry is generated from MSB
1

## Slide 4
Example 1 (16 bit) :
ADD BX, CX where BX = 0212 H and CX= 1251 H
0212 h =
0 0 0 0 0 0 1 0 0 0 0 1 0 0 1 0
BX =
1251 h =
0 0 0 1 0 0 1 0 0 1 0 1 0 0 0 1
CX =
0 0 0 1 0 1 0 0 0 1 1 0 0 0 1 1
1
1
MSB
LSB
Carry is not generated from MSB
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
0

## Slide 5
Parity Flag (PF)
This flag is normally used to check data transmission errors.
PF = 1 , when the result has even parity, an even number of 1’s
PF = 0 , when the result has odd parity, an odd number of 1’s
Example 1 :
ADD BL, CL where BL = 02 H and CL= 51 H
02 h =
51 h =
+
0 0 0 0 0 0 1 0
0 1 0 1 0 0 0 1
0 0 0 0 0 0 1 1
BL =
CL =
Result has even number of 1’s
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
1
83 h =
81 h =
1 0 0 0 0 0 1 1
0 0 0 0 0 1 0 0
Example 2 :
ADD BL, CL where BL = 83 H and CL= 81 H
BL =
CL =
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
1
1
1
Result has odd number of 1’s
0
1 0 0 0 0 0 0 1

## Slide 6
Auxiliary Carry Flag (AF)
It is a carry generated from lower nibble to upper nibble.
AF = 1 , if carry or borrow generated from lower nibble to upper nibble.
AF = 0 , if carry or borrow not generated from lower nibble to upper nibble.
8 bit data
02 h =
0 0 0 0 0 0 1 0
LB – Lower Nibble
HB – Higher Nibble
16 bit data
0212 h =
0 0 0 0 0 0 1 0 0 0 0 1 0 0 1 0
LB – Lower Nibble
HB – Higher Nibble
ADD BL, CL where BL = 02 H and CL= 51 H
02 h =
51 h =
+
0 0 0 0 0 0 1 0
0 1 0 1 0 0 0 1
0 0 0 0 0 0 1 1
BL =
CL =
Carry is not generated from lower nibble to higher nibble.
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
0

## Slide 7
ADD BL, CL where BL = 08 H and CL= 58 H
08 h =
58 h =
+
0 0 0 0 1 0 0 0
0 1 0 1 1 0 0 0
0 0 0 0 0 0 0 0
BL =
CL =
1
Carry is generated from lower nibble to higher nibble.
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
1
Example 1 (16 bit) :
ADD BX, CX where BX = 0082 H and CX= 1281 H
0212 h =
0 0 0 0 0 0 0 0 1 0 0 0 0 0 1 0
BX =
1251 h =
0 0 0 1 0 0 1 0 1 0 0 0 0 0 0 1
CX =
0 0 0 1 0 0 1 1 0 1 1 0 0 0 1 1
1
Carry is generated from lower nibble to higher nibble.
AF = 1

## Slide 8
Zero Flag (ZF)
This flag is normally used to check the result of operation is zero or non zero.
This flag is monitor in Compare instruction.
ZF = 1 , when the result consist all bits zero
ZF = 0 , when the result is non zero which means at least one bit is 1.
Example 1 :
SUB BL, CL where BL = 02 H and CL= 02 H
02 h =
02 h =
-
0 0 0 0 0 0 1 0
0 0 0 0 0 0 1 0
0 0 0 0 0 0 0 0
BL =
CL =
Result has all zero
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
1
83 h =
81 h =
1 0 0 0 0 0 1 1
0 0 0 0 0 1 0 0
Example 2 :
ADD BL, CL where BL = 83 H and CL= 81 H
BL =
CL =
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
1
1
1
Result is non zero
0
1 0 0 0 0 0 0 1

## Slide 9
Sign Flag (SF)
MSB of the result is used to indicate whether the result is positive or negative.
SF = 0 , result is positive number
SF = 1 , result is negative number
ADD BL, CL where BL = 02 H and CL= 51 H
02 h =
51 h =
+
0 0 0 0 0 0 1 0
0 1 0 1 0 0 0 1
0 0 0 0 0 0 1 1
BL =
CL =
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
0
- - - - - - - -
S
0
1
+ ve
- ve
MSB
LSB
-23 h
-31 h
+
- 54 h
1101 1101
1100 1111
1010 1100
U | U | U | U | OF | DF | IF | TF | SF | ZF | U | AF | U | PF | U | CF
1

## Slide 10
Trap Flag (TF)
Setting TF puts the processor into single step mode for debugging.
In single stepping, microprocessor executes a instruction and enters into single step ISR.
After that user can check registers or memory contents, if found ok, he/she will proceed the further, else necessary action will be taken.
This utility is called as debug the program.
if TF=1 , the CPU automatically generates an internal interrupt after each instruction, allowing a program to be inspected as it execute instruction by instruction.
TF = 1 , tarp on ( single instruction execution)
TF = 0 , trap off ( all instructions execution)
TF = 0 , trap off
MOV BL, 02h
MOV CL, 02h
ADD BL, CL
AL =
BL =
CL =
DL =
Memory
Registers
Processor execute all instructions and displays output
04
02
TF = 1 , trap ON
MOV BL, 02h
MOV CL, 02h
ADD BL, CL
AL =
BL =
CL =
DL =
Memory
Registers
Processor instruction one by one and wait
02
02
04

## Slide 11
Interrupt Flag (IF)
What is an interrupt???
Ans : To disturb regular flow of processor execution
Fire alarm…….
Processor is busy with its regular execution
Processor will execute this current instruction and then entertain the interrupt
Program
ISR
RET
Interrupt
If user sets IF flag, the CPU will recognize external (maskable) interrupt requests.
Clearing IF disables these interrupts.
IF = 1 , interrupt enabled.
IF = 0 , interrupt disabled.

## Slide 12
Overflow Flag (OF)
It indicates an overflow from the magnitude to the sign bit of result.
If OF is set, an arithmetic overflow has occurred, that is a significant bit has been lost because the size of the result exceeded the capacity of its destination location.
In 8086 interrupt on overflow instruction is available that will generate an interrupt in this situation.
OF = 1 , signed overflow occur
OF = 0 , no overflow

## Slide 13
Number System
Signed Numbers
Unsigned Numbers
No sign i.e. no + ve nor - ve
Positive & Negative
+ ve & - ve
they assume to be positive

## Slide 14
Unsigned Numbers
All Positive numbers
Example : Roll Number
For Unsigned numbers if magnitude is 8 then,
28 = 256
i.e. total 256 + ve numbers are used
Range for unsigned numbers
00 | 0000 0000
01 | 0000 0001
FF | 1111 1111
- - - - - - - -
8 Magnitude
If 8 bit number
BACK

## Slide 15
Signed Numbers
Positive & Negative
+ ve & - ve
How to find whether number is + ve or - ve?
- - - - - - - -
Answers :
MSB
LSB
If MSB of number is 0 then + ve
If number is
8 bit
- - - - - - - -
S
0
1
+ ve
- ve
7 Magnitude
If MSB of number is 1 then - ve
For signed numbers if magnitude is then 7 ,
27 = 128
i.e. 128 - ve numbers & 128 + ve numbers
0 to 127
-128 to -1
Range for +ve and –ve numbers

## Slide 16
Range for Positive numbers ( 0 to 127)
00 | 0000 0000
01 | 0000 0001
7F | 0111 1111
Range for Negative numbers ( - 80 to -01)
80 | 1000 0000
FF | 1111 1111
Range for +ve and –ve numbers

## Slide 17
What is unsigned and signed number following binary ?
1 0 0 0 0 0 1 1
Signed
Unsigned
83 H
03 H
- ve number means 2’s complement of given number
+ 24 h
0010 0100
2’s complement of 24 i.e. -24
1101 1100
Shortcut for 2’s complement : copy number as it is from right side till gets first 1 after 1 complement all numbers
example 1 :
example 1 :
+ 5 h
0101
2’s complement of 05 i.e. -5
1011
7D H
NEXT

## Slide 18
Why 2’s complement is used ?
1 0 0 0 0 0 1 1
If we consider 1 for –ve number
7 bit magnitude then
-03 H
1 0 0 0 0 0 0 1
If we consider 1 for –ve number
7 bit magnitude then
-01 H
1 0 0 0 0 0 0 0
If we consider 1 for –ve number
7 bit magnitude then
- 00 H
Which is not possible
Example Without using 2’s complement just put 1 for negative
To avoid above problem 2’s complement is used
NEXT

## Slide 19
Why 2’s complement is used ?
It is universal method to store –ve number
Anything is 2’s complement of anything (any number)
0 0 0 0 0 0 0 0
2’s complement of 0 is :
0 0 0 0 0 0 0 0

## Slide 20
Overflow Flag :
Overflow flag matters only for signed numbers
Range for Positive numbers ( 0 to 127)
00 | 0000 0000
01 | 0000 0001
7F | 0111 1111
Range for Negative numbers ( - 80 to -01)
80 | 1000 0000
FF | 1111 1111
1111 1111
01
0000 0001
-01
1000 0000
80
1000 0000
-80
Range for Positive numbers : 00 to 7F
Range for Negative numbers : FF to 80
After addition if result is going beyond above ranges then overflow flag is set i.e. OF = 1

## Slide 21
Example for overflow flag:
Overflow flag matters only for signed numbers
23 h
31 h
+
54 h
0010 0011
0011 0001
0101 0100
CY AC OF P
0
0
0
0
27 h
39 h
+
60 h
0010 0111
0011 1001
0110 0000
CY AC OF P
0
0
0
1
42 h
43 h
+
85 h
0100 0010
0100 0011
1000 0101
CY AC OF P
0
0
1
0
-23 h
-31 h
+
- 54
1101 1101
1100 1111
1010 1100
CY AC OF P
1
1
0
1
-27 h
- 39 h
+
- 60 h
1101 1001
1100 0111
1010 0000
CY AC OF P
1
1
0
1
-42 h
-43 h
+
-85 h
1011 1110
1011 1101
0111 1011
CY AC OF P
1
1
1
1
1.Using MSB bit we can identify whether number is +ve or –ve
2. If MSB is 1 it means number is – ve
3. But sometimes it will give wrong sign bit
4. In such cases checking only MSB is not sufficient
5. We have to check range of both numbers
6. If number cross range it means there is overflow problem
Range for Positive numbers : 00 to 7F
Range for Negative numbers : FF to 80
Example :
7F h
01 h
+
80 h
0111 1111
0000 0001
1000 0000
Result is positive and answer gives sign bit negative.
( 0 to 127)
(-80 to -01)

## Slide 22
How processor will identify the overflow because range concept is not applicable for processor
1 = Overflow
0 = not overflow
OF
Formula used by processor is :
C7
+
C6
Processor will come to know the overflow flag using carry
Answers :
23 h
31 h
+
54 h
0 0 1 0 0 0 1 1
0 0 1 1 0 0 0 1
0 1 0 1 0 1 0 0
C0
C1
C2
C3
C4
C5
C6
C7
OF =
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
X-OR table

## Slide 23
Example for overflow flag:
Overflow flag matters only for signed numbers
23 h
31 h
+
54 h
0010 0011
0011 0001
0101 0100
CY AC OF P
0
1
0
0
27 h
39 h
+
60 h
0010 0111
0011 1001
0110 0000
CY AC OF P
0
1
0
1
42 h
43 h
+
85 h
0100 0010
0100 0011
1000 0101
CY AC OF P
0
0
1
0
-23 h
-31 h
+
- 54 h
1101 1101
1100 1111
1010 1100
CY AC OF P
1
1
0
1
-27 h
- 39 h
+
- 60 h
1101 1001
1100 0111
1010 0000
CY AC OF P
1
1
0
1
-42 h
-43 h
+
-85 h
1011 1110
1011 1101
0111 1011
CY AC OF P
1
1
1
1
C7 | C6 | OF
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
X-OR table
C7
+
C6
OF =