## Slide 1: Memory Segmentation of 8086

## Slide 2
Problem : Memory accessed by 8085
Code
Stack
Data
Memory
Memory and Processor are the different chips.
Memory is used to stored code, stack and data.
Code is referred as a program which is always stored in sequence.
Data can stored in any direction.
Stack is used to stored the data in last in first out manner.
Program
0000
FFFF
At some point they all are going to overwrite each other.
Solution :
Memory is divided into different parts which called as segments to automatically prevent the overwriting .
In 8086 memory segmentation concept was invented to avoid overwriting.
Extra
1 MB
Programmers are responsible to create the segments at the time of initialization when start the program.
Processor is responsible to manage the segments (avoid overwriting)

## Slide 3
Files and fodders are the example of segmentation.
There are two types of addresses :
Virtual address
Physical address
File/folder name is virtual address-known to programmer
Actual location in memory is physical address – unknown to programmer.

## Slide 4
Memory
00000
FFFFF
Code
Stack
Data
Extra
If address bus size is 8 bit then we have 28 = 256 unique address of memory locations.
If address bus size is 16 bit then we have 216 = 65535 = 64k memory locations.
If we want 1MB memory hence 8086 having 220 = 1MB i.e. 20 bit address bus.
PA = 12345
0001 0010 0011 0100 0101 = 20 bit
Individual memory location size is 8 bit.
Hence the address bus size is 20 bit then 2 and ½ memory locations are required to store one instruction in case of 8086.
Which means wastage of ½ byte.
If 16 bit address bus then no wastage of memory locations.
We want 20 bit address bus to increase the memory size
We want 16 bit address to provide equal memory locations
To achieve this we are going to use 16 bit virtual address which will converted into 20 bit physical address.

## Slide 5
Memory
00000
FFFFF
Code
Stack
Data
Extra
Segment Addr
Offset Addr
Virtual address = segment address + offset address
16 bit
Both are 16 bit which means compatible.
16 bit
Segment Addr gives the starting address of segment
Offset Addr gives the location which is present at that segment.
Example :
College
CSE
IT
CIVIL
Departments
C01
C02
C03
I01
I02
I03
CI01
CI02
CI03
Segment Addr = Department Name
offset Addr = roll number
To call particular student from college
To call C01
Segment Addr = C
offset Addr = 01
To call C03
Segment Addr = C
offset Addr = 03
No need to change segment address when location is in same segment

## Slide 6
There are three addresses :
Physical address
2. Segment address
3. Offset address
Not given by programmer
Part of virtual address which is given only once
Part of virtual address which is changed.

## Slide 7
Memory
00000
FFFFF
Code
Stack
Data
Extra
0000
FFFF
Offset addresses are limited they are starting with 0000 to FFFF because they are 16 bits.
0000
FFFF
0000
FFFF
0000
FFFF
Maximum size of segment
= 216 = 26 X 210 = 64 X 1KB = 64 KB
Seg reg | Off reg
CS | IP
SS | SP & BP
DS | SI
ES | DI
8086
8086 having segment registers which are used to store the segment address and offset address of memory
When processor wants to execute instruction from memory CS and IP is given
1000
2345
Processor having 20 bit address bus
20 bit address bus
Processor gives the physical addr
Which is 20 bit
PA = Seg x 10H + offset
PA = Seg x 10H + offset
1000 x 10H + 2345
10000 + 2345
PA = 12345 H
12345 H

## Slide 8
Memory
10000
7FFFF
Code
Stack
Data
Extra
0000
FFFF
0000
FFFF
0000
FFFF
0000
FFFF
If CS is 1000 then Code segment will actually start with 10000
Seg reg | Off reg
CS | IP
SS | SP & BP
DS | SI
ES | DI
8086
1000
2345
CS =1000
If SS is 3000 then Code segment will actually start with 30000
3000
30000
SS =3000
If DS is 5000 then Code segment will actually start with 50000
50000
DS =5000
If ES is 7000 then Code segment will actually start with 70000
70000
ES =7000
1FFFF
3FFFF
5FFFF
Suppose we want to start DS from any random number
54210
DS= 5421
34670
DS= 3467
52345
DS= ???
*****A segment can not begin at any location you want, it has to begin at location which is multiple of 10

## Slide 9
What is the minimum size of segment ????
Seg reg | Off reg
CS | IP
SS | SP & BP
DS | SI
ES | DI
8086
5234
52340
Data segment starts with 52340 in memory
We want only this locations after this we want next segment i.e. extra segment.
What is the next segment address????
52341
Because it is not multiple by 10
52342
52342
52343
5234F
52350
Because it is multiple by 10
Minimum size of segment is
16 bytes.
16 = 10 H

## Slide 10
Memory Segmentation of 8086 for exam