## Slide 1: Interrupt mechanism

## Slide 2
Microprocessor/ Microcontroller
Device 1
Device 2
Device N
service
service
service
A single microcontroller can serve several devices. There are two methods to provide services are :

## Slide 3
Interrupt :
In interrupt method, whenever any device needs its service, the device notifies the microcontroller by sending it an interrupt signal
Upon receiving an interrupt signal, the microcontroller interrupts whatever it is doing and serves the device.
Program associated with interrupt is called as ISR (interrupt service routine) .
Advantage of interrupt is that the microcontroller can serve many device as per priority.
In this method microcontroller can ignore the interrupt request of device
ISR (Interrupt Service Routine :
For every interrupt, there must be an interrupt service routine (ISR), or interrupt handler.
When an interrupt invoked, the microcontroller runs the interrupt service routine.
Program
ISR
RETI
Interrupt

## Slide 4
Program
ISR
RET
Interrupt
A processor is busy with its program execution
An interrupt is occurred during the execution
An interrupt is a condition that make the processor to execute ISR
Program is stored into the Code segment and IP is used to give the offset address
CS:
IP
There are n interrupts i.e. 256 (0-255)
INT n
Whenever interrupt occurred processor will executes its current instruction and entered into the ISR of respective interrupt.
For this processor assign ISR Addr to IP.
IP = ISR Addr
Then processor executes the ISR of respective interrupt
After completion of ISR processor has to return to the main program and for that it requires return address (RA)
RA
IP = Return Addr
To get return address processor has to save this next instruction address or return address.
Before entering into ISR of respective interrupt processor will save next instruction address i.e. RA on to the stack.
PUSH Return Addr
And when processor returns from the ISR execution it will refer the saved return address.
POP Return Addr

## Slide 5
Program
ISR
Interrupt
It is not always necessary that, ISR and main program are in the same code segment
When ISR and main program are in the same code segment it is called as intra segment
Normal jumps of 8086 can be in intersegment or intra segment
CS:
IP
INT n
RA
PUSH CS
PUSH IP
When ISR and main program are in the different code segment it is called as intersegment
Only IP will change CS will remains same
IP and CS both will change.
*** but every 8086 interrupt is in intersegment branch. Which means CS and IP both will change.
Return Addr
ISR Addr
CS
IP
POP CS
POP IP
Return Addr
CS
IP
Return Addr

## Slide 6
Program
ISR
Interrupt
CS and IP are the 16 bit registers are used to store 16 bit number
CS:
IP
INT n
RA
PUSH CS
PUSH IP
There are total 256 interrupts and processor has to remember addresses of all interrupts ISR
Return Addr
ISR Addr
CS
IP
POP CS
POP IP
Return Addr
CS
IP
Return Addr
CSH | CSL
CS
IPH | IPL
IP
SP – 4 | IPL
SP – 3 | IPH
SP – 2 | CSL
SP – 1 | CSH
To store those addresses IVT is used i.e. Interrupt Vector Table
*** IVT is not used to store ISR of an interrupt. It is used to store address of that ISR .*****
IVT is also stored into the memory*******

## Slide 7
IPL | INT 0
IPH | 
CSL | 
CSH | 
45 | INT 1
23 | 
00 | 
10 | 
 | INT 255
IVT
00000H
Whenever interrupt occurred, processor save the next instruction address and first go to the IVT
From IVT processor will take the ISR address and then it will jump to that ISR for execution.
00001H
00002H
00003H
00004H
00005H
00006H
00007H
CS = 1000
IP = 2345
For example, INT 1 interrupt occurred, and ISR address of this interrupt is 12345 H

## Slide 10
Program
ISR
RET
Interrupt
IRET
RET : This instruction is used for normal branching
IRET : This instruction is used for Interrupt branching
also it used to reset the IF flag.
When processor entertained an interrupt before executing ISR, Processor make IF = 0, to inform about the interrupt execution.
Which means at a time only one interrupt will execute.

## Slide 11
8086
NMI
INTR
(V)
(NV)
(V)- Vectored- fixed ISR
(NV)- Non Vectored – not fixed ISR – 255 (interrupt)
Mouse
Keyboard
8259
IR0
IR7
INTA
8086 has two interrupt pins:
NMI – Non maskable interrupt (NMI) is a vectored interrupt which means every ISR has a fixed ISR address in vectored table.
INTR – INTR is maskable non vectored interrupt where ISR of this interrupt is available anywhere in the memory. There is fixed ISR address.
with INTR pin 255 interrupts can be connected.
To manage 255 (00-FF) interrupt request there is an external chip interface with 8086 is called as programmable interrupt controller (PIC) – 8259.
8259 is responsible to handle interrupt request and transfer it to the processor through INTR pin.
After receiving interrupt on ISR processor ask vector number by sending two INTA signals.
On first INTA signal 8059 calculates ISR address and on second INTA pulse 8259 send 8 bit vector number on data bus.
‘n’ 8-bit data
Accept Interrupt on behalf of 8086 is the main job of 8259 PIC.
8259 is not responsible for ISR execution.

## Slide 12
8259 has important properties :
Priority
Trigger
Masking
Vector No.
P T M V
8086
NMI
INTR
(V)
(NV)
8259
IR0
IR7
INTA
Highest Priority
Lowest Priority
Default Priorities
Processor can change priority by sending commands.
Processor can change triggering of an interrupt by sending commands. (edge or level)
Processor can mask or unmask of an interrupt by sending commands.
Processor can send vector number of interrupts by sending commands.
Commands
At the time of initialization processor will send interrupt vector number hence, 8259 initialization is compulsory and very important.
Since there are 8 IR, during initialization you have to send only first vector no. for IRO, remaining vector numbers are taken automatically in sequence.
Vector No. for IR0 = 40H
----II------------- IR1 = 41 H
.
.
Vector No. for IR7 = 47H
8259 is used to increase the interrupt and single 8259 chip having only 8 interrupt connection hence cascading is used.
8259
Master
8259
Slave
IR0
1 Master X 8 Slaves X 8 interrupts = 64 interrupts

## Slide 14
0
0
0
0
0
0
0
0
IRR
Interrupt
Request
Register
(8 bit)
0
0
0
0
0
0
0
0
ISR
In
Service
Register
(8 bit)
Interrupt Mask Register(8 bit)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Priority
Resolver
Register
Pin
IR0
IR1
IR2
IR3
IR4
IR0
IR1
IR2
IR3
IR4
IR7
IR5
IR6
IR7
IR5
IR6
When interrupt occurred, which option is selected???? Pin or bit ?????
When two interrupts are occurred, at a time?????
As per priority IR0 having highest priority than IR2 so interrupt request is send for IR0 and being serviced.
IR0 pin goes low
As per priority IR0 having highest priority than IR2 so interrupt request is send for IR0 and IR0 bit set in ISR reg.
But IR2 pin remains high because we don’t know how much time will take by ISR of IR0 for execution.
BIT
1
1

## Slide 15
0
0
0
0
0
0
0
0
IRR
Interrupt
Request
Register
(8 bit)
0
0
0
0
0
0
0
0
ISR
In
Service
Register
(8 bit)
Interrupt Mask Register(8 bit)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Priority
Resolver
Register
IR0
IR1
IR2
IR3
IR4
IR0
IR1
IR2
IR3
IR4
IR7
IR5
IR6
IR7
IR5
IR6
2. When interrupt occurred on any line, the corresponding bit will be set in IRR register.
1
3. IRR send request to processor through INT pin which is connected with INTR of processor.
1. All bits of all three registers are 0 means there is no interrupt request, no interrupt is being serviced and no masked interrupt
4. Once received acknowledgement from processor through INTA bar pin 8259 set respective bit of ISR
1
Process when there is only one interrupt request

## Slide 16
0
0
0
0
0
0
0
0
IRR
Interrupt
Request
Register
(8 bit)
0
0
0
0
0
0
0
0
ISR
In
Service
Register
(8 bit)
Interrupt Mask Register(8 bit)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Priority
Resolver
Register
IR0
IR1
IR2
IR3
IR4
IR0
IR1
IR2
IR3
IR4
IR7
IR5
IR6
IR7
IR5
IR6
2. First interrupt occurred on IR0 line, the corresponding bit will be set in IRR register.
1
4. Second interrupt occurred on IR4 line.
1. All bits of all three registers are 0 means there is no interrupt request, no interrupt is being serviced and no masked interrupt
6. In this situation 8259 follows default priority if there is no programmable priority.
1
Process more than one interrupt requests simultaneously.
5. IR4 is also set in IRR.
1
Which interrupt should get first priority??????
7. IR0 having highest priority that IR4, hence 8259 will send interrupt request for IR0 and make IR0=1 in ISR after receiving acknowledgement from processor.
8. After completion of IR0 ISR execution 8259 will send interrupt request for IR0

## Slide 17
0
0
0
0
0
0
0
0
IRR
Interrupt
Request
Register
(8 bit)
0
0
0
0
0
0
0
0
ISR
In
Service
Register
(8 bit)
Interrupt Mask Register(8 bit)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Priority
Resolver
Register
IR0
IR1
IR2
IR3
IR4
IR0
IR1
IR2
IR3
IR4
IR7
IR5
IR6
IR7
IR5
IR6
2. IR1 has accrued.
1
3. 8259 will check priority within IRR register. And according to default priority IR1 priority > IR 4 priority, hence 8259 consider IR1
1. Currently IR2 is being serviced, and IR 4 is in waiting state.
5. 8259 send interrupt request for IR1
1
Process when one interrupt being serviced, one interrupt in waiting state and one more interrupt occurred.
4. 8259 also compare the being serviced IR priority with requested IR priority.
1
**** IMP****
7. Now processor call ISR of IR1 execute it and return to IR2 and execute it.
IR2 < IR1
6. On first INTA bar pulse processor ask vector no. and on second clock pulse 8259 provide vector no. for IR 1 and set IR1 in In Service reg.
1

## Slide 18
0
0
0
0
0
0
0
0
IRR
Interrupt
Request
Register
(8 bit)
0
0
0
0
0
0
0
0
ISR
In
Service
Register
(8 bit)
Interrupt Mask Register(8 bit)
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Priority
Resolver
Register
IR0
IR1
IR2
IR3
IR4
IR0
IR1
IR2
IR3
IR4
IR7
IR5
IR6
IR7
IR5
IR6
2. IR3 has accrued.
1
3. 8259 will check priority within IRR register and according to default priority IR3 priority > IR 5 priority, hence 8259 consider IR3
1. Currently IR4 is being serviced, and IR5 is in waiting state.
1
Process when one interrupt being serviced, one interrupt in waiting state and one more interrupt occurred but one of them is maskable.
4. 8259 also compare the being serviced IR priority with requested IR priority.
1
**** IMP****
7. In this example IR3 is maskable interrupt which means processor is not interested to in this interrupt hence 8259 make 0 for IR3 in IRR.
6. Before above comparison 8259 first check whether requested interrupt is masked or not
0

## Slide 19
Processor
8059
Slave 0
IR0
IR0
CD
8059
Slave 1
IR1
IR0
Floppy
IR2
IR3
IR7
8059
Slave 7
IR0
Printer
Keyboard
IR4
IR5
IR6
40
41
42
43
44
45
46
47
Mouse
70
0
0
0
0
0
0
0
50
0
0
0
60
0
0
0
0
0
0
0
INTA
001
CAS0 CAS1 CAS2
000
8259 Master
INTA
INTA
INTA
007
000
0 0 0
000
000
000
50
50

## Slide 25
Processor
8059
Slave 0
IR0
IR1
Printer
8059
Slave 1
IR1
IR2
Usb
IR2
IR3
IR7
8059
Slave 5
IR0
Keyboard
IR4
IR5
IR6
20
21
22
23
24
25
26
27
70
0
0
0
0
0
0
0
40
50
0
0
0
0
0
0
0
INTA
001
CAS0 CAS1 CAS2
000
8259 Master
INTA
INTA
INTA
005
000