## Slide 1: Ch-1 The 8086 microprocessor

## Slide 2
The microprocessor is the central unit of a computer system that performs arithmetic and logic operations, which generally include adding, subtracting, transferring numbers from one area to another, and comparing two numbers.
It's often known simply as a processor, a central processing unit, or as a logic chip.
A microprocessor is an electronic component that is used by a computer to do its work.
It is a central processing unit on a single integrated circuit chip containing millions of very small components including transistors, resistors, and diodes that work together.
Microprocessor

## Slide 3: Evolution of Microprocessor

## Slide 4
Processor
Memory
Programmer write a program using HLL or ALP(instructions)
Assembler will convert HLL/ALP into machine code.(opcode of instructions (hex))
Loader is responsible to load program into memory (binary form)
0000
0001
0002
FFFF
* Individual location size of memory is always 1Byte i.e. 8 bits.
* Entire memory size of memory is depend upon the address bus size of processor.
Processor calculates the memory address and fetch the content of that memory location.
Processor decodes the fetched instruction and execute it.
Content of memory location can be Data/instructions
Basic Functions of processor
Address bus / Data bus

## Slide 5
Features of 8086
Basic Features
Special Features
Miscellaneous Features
Explain features of 8086 ( each for 2 marks)

## Slide 6
Basic Features
Processor Size
Speed of processor
Address bus size for memory
Address bus size for I/O

## Slide 7
2. Special Features
8086 is a pipelined processor
8086 can operate in 2 modes
8086 uses memory banks
8086 uses memory segmentation
8085
Fetch
Decode
Execute
8086
F
D
E
F
D
E
At a time only 1 instruction
At a time 2 instruction

## Slide 9
3. Miscellaneous Features
Interrupts
Registers
Instruction set
Data size for ALU

## Slide 10: Architecture of 8086
Draw and explain architecture of 8086
Diagram –
Explanation –
Draw architecture of 8086 and explain any one unit
Diagram –
Explanation –
Draw architecture of 8086 ( 3 marks)
Main task of Processor :
Fetch
Decode
Execute
To understand any architecture we must know :
How do you fetch the instruction?
Where is getting decoded?
Where is getting executed?

## Slide 11
(16 )
(16 )
(16 )
(16 )
(16 )
(8 )
(8 )
(8 )
(8 )
AX (16 )
BX (16 )
CX (16 )
DX (16 )
(8 )
(8 )
(8 )
(8 )
(16 )
(16 )
(16 )
(16 )
6 Bytes
BUS INTERFACE UNIT
EXECUTION UNIT
8086 is 16 bit processor
(16 )
(16 )
(16 )
Why in two parts????
Pipelining
ALU
PA= seg x 10h + offset

## Slide 12
Pipelining :
8085
Fetch
Decode
Execute
8086
F
D
E
F
D
E
At a time only 1 instruction
At a time 2 instruction
Pipelining is one of the special feature of 8086 processor.
Due to pipelining 8086 processor architecture is divided into two parts.
BIU will fetch the instruction from memory and it will pass that fetched instruction to the Execution unit.
While execution unit executes the current instruction BIU will fetch the next instruction.
Pipelining helps in order to increase the speed of processor.
Back

## Slide 13
Σ
In the architecture diagram of 8086 everything is in rectangle except two following shapes.
This the diagram of arithmetic circuit.
In the given circuit there are two inputs which are used to take operand values.
operation will be performed on input operands and it will produce output.
For example 3 + 4
Operand 1
Operand 2
Output
3
4
3 + 4
7
Back
***In the architecture of 8086 there are two such type of circuits are available from that one is ALU who is responsible to perform arithmetic operations and another one is to calculate memory address.

## Slide 14
There is an instruction ADD AL, BL ( wants to add content of AL reg with content of BL register)
Memory
This instruction will be loaded into the memory
ADD AL, BL
0000
0001
0002
FFFF
Processor will fetch this instruction from memory and to perform fetching processor has to calculate the physical address of that memory location.
Hence arithmetic circuit in upper section is responsible to calculate the physical address of memory location where instruction is stored.
ALU which is present at lower section i.e. in execution unit is responsible to perform actual addition of reg AL and BL data.
How to calculate physical address ????????

## Slide 15
Formula to calculate physical address of memory location is :
PA= Seg x 10h + offset
Overview of memory segmentation:
Memory
This is entire memory supported by 8086.
The amount of memory that you can access is depend upon the address size of processor. 8086 has 20 bit address bus hence entire memory size is 1 MB
00000
FFFFF
Example :
If you want to access any file from your hard disk you will access that file from file name.
We don’t know the physical address of that file.
We know the logical address i.e. name
In 8086 memory is divided into 4 part i.e. segments
Code
Stack
Data
Extra
If you want to access any location of memory which will have its unique physical address.
We give segment address (starting addr of segment) and
offset addr (location within particular segment)
CS
IP
Ss
SP
DS
SI
Extra
DI
Example :
There is a book which has 1000 pages.
Assume there are 10 chapters and each chapter has 100 pages.
We want to go on page no. 564.
There are two methods :
1
Directly call 564
2
5 th chapter
64 page
CS
IP
Assume: CS= 1000 & IP= 2345
PA = Seg x 10H + offset
1000 x 10H + 2345
10000 + 2345
PA = 12345 H

## Slide 16
Σ
Operand 1
Operand 2
Output
ES (16)
CS (16)
SS (16)
DS (16)
IP (16)
These are the registers which are used to stored starting address of segments
Physical addr
Back

## Slide 17
Functions of BIU :
Fetch the next Instruction from memory
Calculate the Physical Addr
Manage the instruction queue.
Managing of queue :
Processor fetch the next instruction and calculate the physical addr of that instruction.
After PA calculation processor will transfer that instruction into instruction queue through data bus (16 bit). This phase is called as prefetching phase.
Maximum size of instruction queue is 6 bytes.
1
2
3
4
5
6
7
8
9
.
.
EI
6 bytes of program
when EU executing the next instruction BIU fetch the next 6 bytes of program
How many Instructions are in the queue?????
(nobody knows)
How many bytes are in the queue?????
(6 bytes)
All instructions are in different size :
1) ADD BL,CL : 1 byte
2) ADD CL, 02H : 2 bytes
3) ADD AX, 2000H : 3 bytes
Smallest instruction of 8086 is 2 bytes
Biggest instruction of 8086 is 6 bytes

## Slide 18
Smallest instruction of 8086 is 2 bytes
Biggest instruction of 8086 is 6 bytes
8086 has 6 bytes instruction queue
It is FIFO type of queue i.e. First In First Out
Processor will fetch the next 6 bytes and store into the queue. EU removes one by one each byte for execution
When BIU will refill the queue???
1
1
2
3
4
5
6
1
2
3
4
5
6
When first entered element removed for execution
Memory
Queue
First our for execution
First our for execution
2
3
4
5
6
1
After one byte empty
2
When all 6 bytes are transferred
3
When 2 bytes are transferred for execution.
1
2
3
4
When BIU will refill the queue???
When 2 bytes are transferred for execution. Because the smallest instruction of 8086 is 2 bytes

## Slide 19
When pipeline fails ???
1
2
3
4
5
6
Queue
JMP

## Slide 20
(16 )
(16 )
(16 )
(16 )
(16 )
(8 )
(8 )
(8 )
(8 )
AX (16 )
BX (16 )
CX (16 )
DX (16 )
(8 )
(8 )
(8 )
(8 )
(16 )
(16 )
(16 )
(16 )
6 Bytes
8086 is 16 bit processor
(16 )
(16 )
(16 )
Why in two parts????
PA= seg x 10h + offset
Mov BL, 03
Mov CL, 04
Add BL , CL
03
04
1.BIU calculates the physical addr of this instruction (Add BL,CL) and fetch it from memory
2. Instruction will transfer into instruction Queue through data bus
Add BL , CL
Add BL , BL
3. There is a intermediate phase between fetching and executing is called decoding which is done by control system
4.Decoding means identify the operation of an instruction and inform to execution unit about it
Add BL , CL
5. Control System produces signal for reg. BL and CL to inform about the operation.
6. After receiving signal about the operation Reg. BL and CL float there content on data bus and also keep original value.
03
04
7. Control system again inform to ALU about floating data
03
04
8. ALU take both operands and performs addition float the output on database
07
07
07
9. Control system send notification to BL reg about the output because result is always stored into 1st operand register
10. BL replace output with its previous value
07

## Slide 21
Draw and explain architecture of 8086

## Slide 27
Pipelining :
8085
Fetch
Decode
Execute
8086
F
D
E
F
D
E
At a time only 1 instruction
At a time 2 instruction
Pipelining is one of the special feature of 8086 processor.
Due to pipelining 8086 processor architecture is divided into two parts.
BIU will fetch the instruction from memory and it will pass that fetched instruction to the Execution unit.
While execution unit executes the current instruction BIU will fetch the next instruction.
Pipelining helps in order to increase the speed of processor.
Advantages of Pipelining :

## Slide 34: Pin diagram of 8086
For Exam

## Slide 36: 1. Supply Pins (3) :

## Slide 37
2. Clock related Pins (3) :

## Slide 39
3. Address and Data Pins (3) :
0
1
Pass 0 signal and wait
Pass 1 signal and wait
0
1
1 clock cycle = 1 T state
T1
T2
T3
T4
1. Address calculation
A15-A0
Address Bus
2. Data
D15-D0
How to differentiate between data and address ???
Something is high which indicates that bus carries the address.
ALE
When ALE = 1 : Address bus (A15-A0)
When ALE = 0 : Data bus (D15-D0)
Tristate
Buffer
I/P
0
1
O/P
0
1
Buffer
When enable then only output appears on output line
This concept is used in ALE i.e Address Latch Enable (to latch the address